## Slide 1: Creating PRP with the PureSpin® System

## Slide 2: Setting up your workstation
Add anti-coagulant (sodium citrate) to the syringe for blood collection
30cc Kit - 3cc Sodium Citrate
60cc Kit - 5cc Sodium Citrate

## Slide 3: Drawing the blood
Attach syringe to 19g butterfly
19g needle is ideal to decrease the risk of lysing platelets….but it is not always possible
Use a 21g needle in patients with veins not adequate enough to use the 19g

## Slide 4: Remember the 3 T’s
If you initially do not see a “good” vein…..
• Tighten Tourniquet
• Time (Keep tourniquet in place for
2-3 minutes
• Tap the vein to bring it to the
surface

## Slide 5: Place blood in concentrating tube
Luer-lock connectors (twist clockwise). The luer-lock prevents any contaminants from entering the blood.
Red (whole) blood goes in red capped tube

## Slide 6: Slowly add whole blood to collection device, as not to damage platelets

## Slide 7: Place in centrifuge
Balance with water filled counterbalance tube
Weight must be within 4 grams
Place blood in centrifuge bucket opposite counterbalance

## Slide 8: First Spin
30cc Kit
1 Minute @ 4200 RPM
60cc Kit
1.5 minutes @ 3800 RPM

## Slide 9: After first spin, the collection device will look like this….

## Slide 10: Pulling plasma from red cells
Pull plasma from red cells
Pull until you achieve a red flash in the inner tube
Place plasma in second concentrating tube
Weigh the second tube, and prepare counterbalance
Must be within 4 grams
Place in centrifuge bucket opposite counterbalance

## Slide 11: Second Spin
30cc Kit
5 Minute @ 4200 RPM
60cc Kit
5 minutes @ 3800 RPM

## Slide 12: Concentrate the PRP according to the procedure you are performing
Remove the PPP (platelet-poor plasma) and leave the amount of fluid in the tube needed for the procedure.
Swirl the tube to resuspend the platelets into solution.
Pull the newly created platelet-rich plasma into the syringe needed for the injection

## Slide 13: Volumes of PRP for Vampire® Procedures

## Slide 14: Volume of PRP for Musculoskeletal Injections

## Slide 15: Find out how to take your PRP Practice to the next level
www.PerfectPRP.com

## Slide 16: To make an appoint to discuss your PRP needs, or to have a 1–2-hour session with me to get your new centrifuge set-up
calendly.com/drjeff-regen

## Slide 17: Contact Me
Jeffrey Piccirillo, DO
CEO/Founder Regenerative Medical Associates
DrJeff@regenmedicalgroup.com
Cell: 641-990-6737
www.Regenmedicalgroup.com
www.PerfectPRP.com
www.PerfectPRPthebook.com